## Slide 1: 1047
11/06/2023
Juarez Chihuahua.
Incoming Inspection Report

## Slide 2
Tool General Information Identification Plaques.
Injection layout – Hot Runner System ,Plaques, tests .
Layout Cavity Side (Main appearances ).
Slides , Retractors , Lifters Details.
Layout Core Side (Main appearances ) .
Ejector System & Parts .
Locating Ring.
Electrical Plugs .
Water Leaks Test.
Spare Parts , Documents ,Tool manuals etc. Received .
Observations / Summary.
Quick Check List.
Index

## Slide 3: Tool General Information Identification Plaques
01

## Slide 4
Tool Identification plate
Tool Identification | Description
Owner of Tool: | GM
Tool Source: | STAR TECH
Job: | ALNA 1047
Part Number: | 6404000174 / 6404000173
ASSET# | N/A
ALNA Number: | ALNA 1047


## Slide 5
Tool Identification plate
Tool Description | 
mold weight: | 12,050
,mold size (axbxc): | 1030mm x 1662mm x 1500mm
Texture Type: | No
Core Steel Type: | N/A
Cavity Steel Type: | N/A
Sprue Radius: | N/A
Orifice Size: | N/A


## Slide 6: Injection layout – Hot Runner System ,Plaques, tests .
02

## Slide 7
Hot Runner System OERLIKON #H247905.0
Hot Runner System
Zone Hot Nozzle system:
# Zones 42


## Slide 8
Hot Runner System OERLIKON #H247905.0
Hot Runner System
Zone Hot Nozzle system:
# Zones 42


## Slide 9
Hot Runner System Testing
Valve #1open
Valve #2 open
Valve #1 Closed
Valve # 2 Closed

Testing the hot runner system comments:
Heaters tested at 550 ° C, valve pin movement is performed, ok they open and close correctly.

## Slide 10
Hot Runner System Testing
Valve #1open
Valve #2 open
Valve #1 Closed
Valve # 2 Closed

Testing the hot runner system comments:
Heaters tested at 550 ° C, valve pin movement is performed, ok they open and close correctly.

## Slide 11: Layout Cavity Side (Main appearances )
03

## Slide 12

Sectional views:
Cavidad 1
Cavidad 2
Lay outs – Mobile Side

## Slide 13

Sectional views:
Cavidad 3
Cavidad 4
Lay outs – Mobile Side

## Slide 14
Lay outs – Fixed Side

Sectional views:
Cavidad 1
Cavidad 2

## Slide 15
Lay outs – Fixed Side

Sectional views:
Cavidad 3
Cavidad 4

## Slide 16
Tool View

Operator Side
Non Operator Side
Top Side
Bottom Side

## Slide 17: Slides , Retractors , Lifters Details.
04

## Slide 18
Lay outs – Fixed Side
Identification of Mechanisms by Colors
Sliders
Lifters
Recuperators
Leader Pin
Angle pin
Spotting Plaques

Mold Cavity- how many cavity 2

## Slide 19
Lay outs – Mobile Side
Identification of Mechanisms by Colors
Sliders
Lifters
Recuperators
Leader Pin
Greasers
Spotting Plaques
Mold Cavity- how many cavity 2


## Slide 20
Slides, Retractors , Lifters etc.
Mold Have The Following Systems.
Components | Lifters | Recuperators | Sliders | Ejector Sleeves | Ejector Blades | Ejector Pins | Others
Quantity | 12 | 4 | 2 | N/A | 0 | n/a | 
Damages | NO | NO | N/A | N/A | N/A | NO | 
Water Cooling? | NO | NO | N/A | N/A | N/A | N/A | 
Plugs: Press Fit Or Threaded | N/A | N/A | N/A | N/A | N/A | N/A | 
Water Leaks | N0 | N/A | N/A | N/A | N/A | N/A | 
Water Connectors Size | NO | N/A | N/A | N/A | N/A | N/A | 
Welding Marks | NO | NO | N/A | N/A | N/A | NO | 
Movements | YES | NO | YES | N/A | N/A | N/A | 
Fastening With Screws Or Bolts | NO | N/A | N/A | N/A | N/A | N/A | 
Stopper | N0 | N/A | N/A | N/A | N/A | N/A | 
CAM PIN Position | N/A | N/A | N/A | N/A | N/A | N/A | 
Slide Retainer | N/A | N/A | N/A | N/A | N/A | N/A | 
ALNA Standard? | YES | N/A | N/A | N/A | N/A | N/A | 
Additional Comments: |  |  |  |  |  |  | 


## Slide 21: Layout Core Side (Main appearances )
05

## Slide 22
Layout Core Side (main appearences)


## Slide 23: Ejector System & Parts .
05

## Slide 24
Ejector System
First position: Slides & retractors in Position backward
Second position: Slides & retractors in Position forward ( ejection backward)


## Slide 25
Ejector System
Ejection System Has The Following Configuration:
1050mm
blow ejection system
hydraulic ejection system


## Slide 26
Ejector System Parts
No se sacaron expulsores

## Slide 27: Locating Ring.
06

## Slide 28
Locator Ring

Fixed Side

## Slide 29: Electrical Plugs .
07

## Slide 30
Electrical Parts
Conector Plug for HotRunner System.
Connector standard D-M-E per Heater and Thermocouples
42 for heater and 42 for thermocouples
Connector standard for limit switch D-M-E
Heaters & Thermocouple.
Limit Switch Connector


## Slide 31: Water Leaks Test
08

## Slide 32
Water Leak Testing
Mobile side
Fixed side
Cooling tests are performed, result ok without water leaks.


## Slide 33: Spare Parts , Documents ,Tool manuals etc. Received .
09

## Slide 34
1 | Folder
1 | Usb
1 | Hot System
3 | Centering ring
4 | Cables for controller
Spare Parts, Documents, Tool Manual Received.

## Slide 35: Observations / Summary.
10

## Slide 36
Observations
The Ejector System Is Working. Okay
The Hot System Works Ok
Mirror Areas Okay
Alna Estándar Okay
Coolingsystem core side / cavity side Ok
Texture área: Okay

## Slide 37
Observations
Ejector System

Hydraulic system connectors are changed

## Slide 38
Observations
Damaged sliders

The ejection system is located in the fixed part of the mold. The mold was received with the fixed part up, when opening the mold we realized that the ejector plate was in the front (ejectors and lifters out of position) which cause the sliders to collide with the ejector

## Slide 39
Observations
Repaired sliders

Damaged sliders are repaired

## Slide 40
Observations
Damaged ejector

Ejectors damaged by Lifters

## Slide 41
Observations
Change of Staubli

Connectors from M6 to M8 are placed

## Slide 42: Quick Check List.
11

## Slide 43
Quick Checklist
L# | DESCRIPTION | YES | NO | N/A | COMMENTS / OBSERVATIONS
1 | LOCATING RINGS | x |  |  | 
2 | AIR VENTS & ITS DEPTH | x |  |  | 
3 | INTERLOCKS ( PARTING LINE LOCKS ) |  | x |  | 
4 | DATE INSERTS OR ENGRAVING | x |  |  | 
5 | HOT RUNNER SYSTEMS NUMBER | x |  |  | H247905.0
6 | THERMOCOUPLE & RESISTANCE SPARES | x |  |  | 
7 | EJECTOR BLADES |  | X |  | 
8 | VALVE GATES AVAILABILITY | x |  |  | 
9 | ANGLE PINS FOR SLIDES | x |  |  | 
10 | LOCKING CYLINDERS AVAILABILITY |  | X |  | 
11 | SPRINGS ON EJECTION SYSTEM | X |  |  | 
12 | TEXTURES IN CAVITY | x |  |  | 
13 | IDENTIFICATION ON ALL PARTS | x |  |  | 
14 | HYDRAULIC PISTON FOR CORES | X |  |  | 
15 | LIMIT SWITCHES (MICRO SWITCH) | x |  |  | 
16 | RJG OR SPECIAL SENSORS |  | x |  | 
17 | SAFETY LOCK | x |  |  | 
18 | INSERT CHANGES SPARES |  | X |  | 
19 | MOLD DRAWINGS & CD | x |  |  | 

## Slide 44
Quick Checklist
L# | DESCRIPTION | COMMENTS
1 | MOLD NUMBER | 1047
2 | PART NUMBER | N/A
3 | PART NAME | GM BT1CG HL (INNER LENS)
4 | NO. OF CAVITIES | 4
5 | CAVITIES MARKED NO.'S | NO
6 | TOOLING ENGINEER NAME | Protev
7 | MOLD ARRIVAL DATE | 8/06/2023
8 | MOLD INCOMING INSP. DATE START | 10/06/2023
9 | MOLD INCOMING INSP. DATE FINISH | 11/06/2023
10 | TOTAL ACCUMULATED HOURS | 26hrs
11 | INCOMING INSPECTION STATUS | FINISHED
12 | INCOMING INSPECTION PERFORMED BY | Alberto Ramirez & Lorenzo Lopez
13 | FREQUENCY FOR PM | 
14 | PRESS ASSIGNED | 

## Slide 45: Thanks!