## Slide 1: GM BT1CG HL Light Block 1052
06/05/2023
Juarez Chihuahua.
Incoming Inspection Report

## Slide 2
Tool General Information Identification Plaques.
Injection layout – Hot Runner System ,Plaques, tests .
Layout Cavity Side (Main appearances ).
Slides , Retractors , Lifters Details.
Layout Core Side (Main appearances ) .
Ejector System & Parts .
Locating Ring.
Electrical Plugs .
Water Leaks Test.
Spare Parts , Documents ,Tool manuals etc. Received .
Observations / Summary.
Quick Check List.
Index

## Slide 3: Tool General Information Identification Plaques
01

## Slide 4
Tool Identification plate
BACK TO INDEX
Tool Identification | Description
Owner of Tool: | GMC
Tool Source: | Datrin Mold
Job: | ALNA 180
Part Number: | 6406000265/ 6406000266
ASSET# | 
ALNA Number: | ALNA 180


## Slide 5
Tool Identification plate
Tool Description | 
mold weight: | 2,755 kg
mold size (axbxc): | 1100mm x 750mm x 748.4mm
Texture Type: | No
Core Steel Type: | FS/2343ESR/MS/2343ESR, 48-50HRC
Cavity Steel Type: | FS/2343ESR/MS/2343ESR, 46-49HRC
Sprue Radius: | SR 19.05m
Orifice Size: | D .75 mm


## Slide 6: Injection layout – Hot Runner System ,Plaques, tests .
02

## Slide 7
Hot Runner System OERLIKON #H251248.0
Hot Runner System
Zone Hot Nozzle system:
# Zones 6


## Slide 8
Hot Runner System Testing
Valve #1open
Valve #2 open
Valve #1 Closed
Valve # 2 Closed

Testing the hot runner system comments:
Heaters tested at 500 ° C, valve pin movement is performed, ok they open and close correctly.

## Slide 9: Layout Cavity Side (Main appearances )
03

## Slide 10
Lay outs – Mobile Side
Sectional views:

1
2

## Slide 11
Lay outs – Fixed Side

Sectional views:
The mold has mirror in all cavities
1
2

## Slide 12
Tool View

Operator Side
Non Operator Side
Top Side
Bottom Side

## Slide 13: Slides , Retractors , Lifters Details.
04

## Slide 14
Lay outs – Fixed Side
Identification of Mechanisms by Colors
Sliders
Lifters
Recuperators
Leader Pin
Angle pin
Spotting Plaques
Mold Cavity- how many cavity


## Slide 15
Lay outs – Mobile Side
Identification of Mechanisms by Colors
Sliders
Lifters
Recuperators
Leader Pin
Greasers
Spotting Plaques
Mold Cavity- how many cavity 2


## Slide 16
Slides, Retractors , Lifters etc.
Mold Have The Following Systems.
Components | Lifters | Recuperators | Sliders | Ejector Sleeves | Ejector Blades | Ejector Pins | Others
Quantity | NO | 4 | N/A | N/A | N/A | 28 | 
Damages | NO | NO | N/A | N/A | N/A | NO | 
Water Cooling? | NO | NO | N/A | N/A | N/A | N/A | 
Plugs: Press Fit Or Threaded | N/A | N/A | N/A | N/A | N/A | N/A | 
Water Leaks | N0 | N/A | N/A | N/A | N/A | N/A | 
Water Connectors Size | NO | N/A | N/A | N/A | N/A | N/A | 
Welding Marks | NO | NO | N/A | N/A | N/A | NO | 
Movements | NO | NO | N/A | N/A | N/A | YES | 
Fastening With Screws Or Bolts | NO | N/A | N/A | N/A | N/A | N/A | 
Stopper | N0 | N/A | N/A | N/A | N/A | N/A | 
CAM PIN Position | N/A | N/A | N/A | N/A | N/A | N/A | 
Slide Retainer | N/A | N/A | N/A | N/A | N/A | N/A | 
ALNA Standard? | N/A | N/A | N/A | N/A | N/A | YES | 
Additional Comments: |  |  |  |  |  |  | 


## Slide 17: Layout Core Side (Main appearances )
05

## Slide 18
Layout Core Side (main appearences)
It has no hydraulic system


## Slide 19: Ejector System & Parts .
05

## Slide 20
Ejector System
First position: Slides & retractors in Position backward
Second position: Slides & retractors in Position forward ( ejection backward)


## Slide 21
Ejector System
Ejection System Has The Following Configuration:
1050mm
blow ejection system
hydraulic ejection system


## Slide 22
2 PERNOS EXPULSORES | D=10mm x L=310mm
8 PERNOS EXPULSORES | D=8mm x L=350mm
18 PERNOS EXPULSORES | D=6mm x L=330mm
4 RESORTES AZULES | D.Ext= 39.7mm D.int=20mm x L=175mm
4 RESORTES AZULES | D.Ext= 20mm D.int=10mm x L=25mm
4 SHOULDER | D=40mm x L=62mm / Rosca 16mm
Ejector System Parts

## Slide 23: Locating Ring.
06

## Slide 24
Mobile Side
Fixed Side
Locator Ring
The diameter of the centering rings on the fixed side is 200mm


## Slide 25: Electrical Plugs .
07

## Slide 26
Electrical Parts
Conector Plug for HotRunner System.
Connector standard D-M-E per Heater and Thermocouples
6 for heater and 6 for thermocouples
Connector standard for limit switch D-M-E
Heaters & Thermocouple.
Limit Switch Connector


## Slide 27: Water Leaks Test
08

## Slide 28
Water Leak Testing
Mobile side
Fixed side
Cooling tests are performed, result ok without water leaks.


## Slide 29: Spare Parts , Documents ,Tool manuals etc. Received .
09

## Slide 30
1 | Folder
1 | Usb
1 | Hot System
3 | Centering ring (mobile)
2 | Cables for controller
Spare Parts, Documents, Tool Manual Received.

## Slide 31: Observations / Summary.
10

## Slide 32
Observations
The Ejector System Is Working. Okay
The Hot System Works Ok
Mirror Areas Okay
Alna Estándar Okay
Coolingsystem core side / cavity side Ok
Texture área: Okay

## Slide 33
Observations
Revision of hot runner free of plastic material ok
Expulsion System Review

## Slide 34
Observations
cavities have a Mirror


## Slide 35
Observations
Hot System OK


## Slide 36
Observations
To be able to grease the cores it is necessary to remove cavities

CORES

## Slide 37: Quick Check List.
11

## Slide 38
Quick Checklist
L# | DESCRIPTION | YES | NO | N/A | COMMENTS / OBSERVATIONS
1 | LOCATING RINGS | x |  |  | 
2 | AIR VENTS & ITS DEPTH | x |  |  | 
3 | INTERLOCKS ( PARTING LINE LOCKS ) |  | x |  | 
4 | DATE INSERTS OR ENGRAVING | x |  |  | 
5 | HOT RUNNER SYSTEMS NUMBER | x |  |  | H251248.0
6 | THERMOCOUPLE & RESISTANCE SPARES | x |  |  | 
7 | EJECTOR BLADES |  | X |  | 
8 | VALVE GATES AVAILABILITY | x |  |  | 
9 | ANGLE PINS FOR SLIDES | x |  |  | 
10 | LOCKING CYLINDERS AVAILABILITY | x |  |  | 
11 | SPRINGS ON EJECTION SYSTEM | x |  |  | 
12 | TEXTURES IN CAVITY |  | X |  | 
13 | IDENTIFICATION ON ALL PARTS | x |  |  | 
14 | HYDRAULIC PISTON FOR CORES |  | X |  | 
15 | LIMIT SWITCHES (MICRO SWITCH) | x |  |  | 
16 | RJG OR SPECIAL SENSORS |  | x |  | 
17 | SAFETY LOCK | x |  |  | 
18 | INSERT CHANGES SPARES |  | X |  | 
19 | MOLD DRAWINGS & CD | x |  |  | 

## Slide 39
Quick Checklist
L# | DESCRIPTION | COMMENTS
1 | MOLD NUMBER | 1052
2 | PART NUMBER | 6406000265 / 6406000266
3 | PART NAME | GM BT1CG HL (REFLECTOR)
4 | NO. OF CAVITIES | 2
5 | CAVITIES MARKED NO.'S | NO
6 | TOOLING ENGINEER NAME | Protev
7 | MOLD ARRIVAL DATE | 26/04/2023
8 | MOLD INCOMING INSP. DATE START | 06/05/2023
9 | MOLD INCOMING INSP. DATE FINISH | 08/05/2023
10 | TOTAL ACCUMULATED HOURS | 15hrs
11 | INCOMING INSPECTION STATUS | FINISHED
12 | INCOMING INSPECTION PERFORMED BY | Alberto Ramirez & Juan Puentes
13 | FREQUENCY FOR PM | 
14 | PRESS ASSIGNED | 

## Slide 40: Thanks!