## Slide 1
Incoming Inspection Performed by: Emmanuel Fernandez.
RU OUTER LENS HI LEVEL
Incoming Inspection Report
TOOL MAKER
Juárez , México
DATE: 11-17-2015

## Slide 2
Tool General Information Identification Plaques.
Injection layout – Hot Runner System ,Plaques, tests .
Layout Cavity Side (Main appearances ).
Slides , Retractors , Lifters Details.
Layout Core Side (Main appearances ) .
Ejector System & Parts .
Locating Ring.
Electrical Plugs .
Water Leaks Test.
Spare Parts , Documents ,Tool manuals etc. Received .
Observations / Summary.
Quick Check List.

## Slide 3
IDENTIFICATION
Tool Source : PROPER TOOLING
Job : 14816
Part Number: LH:6002TC0391/RH:6002TC0392
Tool Identification plate

BACK TO INDEX

## Slide 4
MOLD WEIGHT: 19,100 kg.
MOLD SIZE (axbxc): 1320 mm X 1650 mm X
1427.5 mm
Nozzle radius: 19.1 mm
Injection diameter: 5 mm
General Information
Owner of Tool: Chrysler

BACK TO INDEX

## Slide 5
Hot Runner System #
HO95511.0
Hot Runner System
Zone Hot Nozzle system:

BACK TO INDEX

## Slide 6
Hot Runner System Testing
Testing the hot runner system comments:
All Zones Reached Its Proper Temperature, The Valve Is Moved Ok And Testing The Hot Runner System Everything Is Ok!

BACK TO INDEX
all zones of the mold is heated to 560° F.
VALVE CLOSED
VALVE OPENED

## Slide 7
The mold have 2 cavities (RH/LH)
Lay outs – Cavity Side
Mold Cavity – How many Cavity ?

BACK TO INDEX

## Slide 8
Lay out – cavity LH & RH
Frontal View cavities RH & LH. Comments: No damages founded

BACK TO INDEX
CAVITY RH
CAVITY LH

## Slide 9
Slides, Retractors , Lifters etc.
The mold have lifters & slides
 |  |  | COMMENTS
NO. OF SLIDES |  |  | 2
DAMAGES |  |  | NO VISIVLE DAMAGRES
WATER LEAKS |  |  | NO WATER LEAKS
PLUGS - PRESS FIT OR THREADED |  |  | 
STOPPER |  |  | 
WATER CONNECTOR SIZE |  |  | ¼” NPT
MOVEMENTS |  |  | N/A
CAM PIN POSITION |  |  | N/A
SLIDE RETAINER |  |  | N/A

BACK TO INDEX

## Slide 10
Core Layout
Frontal View cores LH& RH, comments:
No visible Damage founded

BACK TO INDEX
LH
RH

## Slide 11
Ejector System

BACK TO INDEX

## Slide 12
Ejector System
Ejector System Tested ? , Back and Forward Position ?
The Ejector System Is Ok!
Ejector system backward position picture
Ejector system forward position picture

BACK TO INDEX

## Slide 13
Ejector system parts and components

BACK TO INDEX

## Slide 14
Locator Ring
How many Locating rings ?
1
Sizes?
138.04 mm

BACK TO INDEX

## Slide 15
Electrical Parts
Conector Plug for Hot Runner System.
Conector standard D-M-E per Heater and Thermocouples ?
for 4 zones
Conector standard For Limit Switch D-M-E?
4 for core #1 float plate and 2 for ejector plate.
heaters and thermocouple.
Limit Switch Connector

BACK TO INDEX

## Slide 16
Water leak Testing
Test Both sides of the tool with water at desired temperature ? comments:
THE CAVITY AND CORE SIDE ARE TESTED AT 85°C , NO WATER LEAKS

BACK TO INDEX
CAVITY SIDE
CORE SIDE

## Slide 17
Spare parts ,Documents , Tool Manual etc. Received
The mold arrived

BACK TO INDEX

## Slide 18
Observations
In the incoming inspection not detected failures
The ejector system is working Ok.
The HRS is Ok.
El molde llega con oxido en zonas perifericas

BACK TO INDEX

## Slide 19
Quick Checklist
BACK TO INDEX
L# | DESCRIPTION | YES | NO | N/A | COMMENTS / OBSERVATIONS
1 | LOCATING RINGS |  |  |  | How many numbers? 1
2 | AIR VENTS & ITS DEPTH |  |  |  | Availability of sufficient number of air vents? YES
3 | INTERLOCKS ( PARTING LINE LOCKS ) |  |  |  | How many? 2
4 | DATE INSERTS OR ENGRAVING |  |  |  | Specify how many years?
5 | HOT RUNNER SYSTEMS NUMBER |  |  |  | 
6 | THERMOCOUPLE & RESISTANCE SPARES |  |  |  | 
7 | EJECTOR BLADES |  |  |  | 
8 | VALVE GATES AVAILABILITY |  |  |  | 
9 | ANGLE PINS FOR SLIDES |  |  |  | 
10 | LOCKING CYLINDERS AVAILABILITY |  |  |  | 
11 | SPRINGS ON EJECTION SYSTEM |  |  |  | Color ? BLUE
12 | TEXTURES IN CAVITY |  |  |  | 
13 | IDENTIFICATION ON ALL PARTS |  |  |  | 
14 | HYDRAULIC PISTON FOR CORES |  |  |  | 
15 | LIMIT SWITCHES (MICRO SWITCH) |  |  |  | 
16 | RJG OR SPECIAL SENSORS |  |  |  | Specify ?
17 | SAFETY LOCK |  |  |  | 
18 | INSERT CHANGES SPARES |  |  |  | 
19 | MOLD DRAWINGS & CD |  |  |  | 

## Slide 20
Quick Checklist
MOLD NUMBER | 14816
PART NUMBER | LH:6002TC0391/RH:6002TC0392
PART NAME | OUTER LENS HI LEVEL
NO. OF CAVITIES | 2
CAVITIES MARKED NO.'S | 
TOOLING ENGINEER NAME | 
MOLD ARRIVAL DATE | 
MOLD INCOMING INSP. DATE | 
FREQUENCY FOR PM | N/A
PRESS ASSIGNED | N/A
BACK TO INDEX