## Slide 1
Incoming Inspection Performed by: José Alberto Pérez
AUDI Q5 HL OUTER LENS
Incoming Inspection Report
TOOL MAKER
Juárez , México
DATE: 04-11-2015

## Slide 2
Tool General Information Identification Plaques.
Injection layout – Hot Runner System ,Plaques, tests .
Layout Cavity Side (Main appearances ).
Slides , Retractors , Lifters Details.
Layout Core Side (Main appearances ) .
Ejector System & Parts .
Locating Ring.
Electrical Plugs .
Water Leaks Test.
Spare Parts , Documents ,Tool manuals etc. Received .
Observations / Summary.
Quick Check List.

## Slide 3
IDENTIFICATION
Tool Source : PROSPECT MOLD
Job : 3312
Part Number: 6002TC0397/98
ALNA Number# 490
Tool Identification plate

BACK TO INDEX

## Slide 4
MOLD WEIGHT : 16,896Kg.
TMOLD SIZE (axbxc): 69”X 53” X
55.5”
Nozzle radius: 19.05mm
Injection diameter : 12mm.
General Information
Owner of Tool: AUDI AG.

BACK TO INDEX

## Slide 5
Hot Runner System #
H091800.0 H091802.0
Hot Runner System
Zone Hot Nozzle system:
1° Clear 17 Zones
1° Black 34 Zones

BACK TO INDEX

## Slide 6
Hot Runner System Testing
Testing the hot runner system comments:
All Zones Reached Its Proper Temperature And Testing The Hot Runner System Everything Is Ok!

BACK TO INDEX
All zones of the mold is heated to 530° F.
2ND SHOT CLEAR
1st. Shot Black

## Slide 7
No visible Damage founded
Lay outs – Cavity Side
Mold Cavity – How many Cavity ?

BACK TO INDEX

## Slide 8
Slides, Retractors , Lifters etc.
MOLD DO NOT HAVE THE FOLLOWING SYSTEMS: SLIDES AND RETRACTORS.
 |  |  | COMMENTS
NO. OF LIFTERS |  |  | 10
NO. OF SLIDES |  |  | 4
DAMAGES |  |  | NO VISIVLE DAMAGRES
WATER LEAKS |  |  | NO WATER LEAKS
PLUGS - PRESS FIT OR THREADED |  |  | THREADED
STOPPER |  |  | 
WATER CONNECTOR SIZE |  |  | ¼” NPT
MOVEMENTS |  |  | N/A
CAM PIN POSITION |  |  | N/A
SLIDE RETAINER |  |  | N/A

BACK TO INDEX

## Slide 9
Core Layout
Frontal View cores LH& RH, comments:
No visible Damage founded

BACK TO INDEX
Station 1
Station 2

## Slide 10
Ejector System
Ejection System Has The Following Configuration:

BACK TO INDEX
Model No. 2.50CP2HCTV14A7.500
Serial No. AF283970 A
Envelope Pressuer: 3000 psi Hyd.
EXPULSION SYSTEM WORKS WITH HYDRAULIC PISTONS

## Slide 11
Ejector System
Ejector System Tested ? , Back and Forward Position ?
The Ejector System Is Ok!
Ejector system backward position picture
Ejector system forward position pictures

BACK TO INDEX

## Slide 12
Ejector system parts

BACK TO INDEX

## Slide 13
Locator Ring
How many Locating rings ?
TREE
Sizes?
130mm

BACK TO INDEX

## Slide 14
Electrical Parts
Conector Plug for Hot Runner System.
Conector standard D-M-E per Heater and Thermocouples ?
10 for 1° Clear 17 Zones & 1° Black 34 Zones
Conector standard For Limit Switch D-M-E?
1 For The Ejector Plate & 1 For The Slides
heaters and thermocouple.
Limit Switch Connector

BACK TO INDEX

## Slide 15
Water leak Testing
Test Both sides of the tool with water at desired temperature ? comments:
THE CAVITY AND CORE SIDE ARE TESTED AT 90°C , NO WATER LEAKS

BACK TO INDEX
CAVITY SIDE
CORE SIDE

## Slide 16
Spare parts ,Documents , Tool Manual etc. Received
the mold arrived with documents & Cd.

BACK TO INDEX

## Slide 17
Observations
In The Incoming Inspection Not Detected Failures
The Ejector System Is Working Ok
The Hrs Is Ok.
No Visible Damage Founded
Cooling System Ok
The Mold Has Pressure Sensors.

BACK TO INDEX
Type 1710B0
Operating T. 125° C

## Slide 18
Quick Checklist
BACK TO INDEX
L# | DESCRIPTION | YES | NO | N/A | COMMENTS / OBSERVATIONS
1 | LOCATING RINGS |  |  |  | How many numbers? 2
2 | AIR VENTS & ITS DEPTH |  |  |  | Availability of sufficient number of air vents? YES
3 | INTERLOCKS ( PARTING LINE LOCKS ) |  |  |  | How many? FOR
4 | DATE INSERTS OR ENGRAVING |  |  |  | Specify how many years? 6 (2015-2020)
5 | HOT RUNNER SYSTEMS NUMBER |  |  |  | H091800.0 H091802.0
6 | THERMOCOUPLE & RESISTANCE SPARES |  |  |  | 
7 | EJECTOR BLADES |  |  |  | 
8 | VALVE GATES AVAILABILITY |  |  |  | 
9 | ANGLE PINS FOR SLIDES |  |  |  | 
10 | LOCKING CYLINDERS AVAILABILITY |  |  |  | 
11 | SPRINGS ON EJECTION SYSTEM |  |  |  | Color ?
12 | TEXTURES IN CAVITY |  |  |  | 
13 | IDENTIFICATION ON ALL PARTS |  |  |  | 
14 | HYDRAULIC PISTON FOR CORES |  |  |  | 
15 | LIMIT SWITCHES (MICRO SWITCH) |  |  |  | 
16 | RJG OR SPECIAL SENSORS |  |  |  | Specify ?
17 | SAFETY LOCK |  |  |  | 
18 | INSERT CHANGES SPARES |  |  |  | ONLY FOR CLOSE DOWN CAVITIES
19 | MOLD DRAWINGS & CD |  |  |  | 

## Slide 19
Quick Checklist
MOLD NUMBER | 3312
PART NUMBER | 6002TC0397/98
PART NAME | AUDI Q5 HL OUTER LENS
NO. OF CAVITIES | 4
CAVITIES MARKED NO.'S | LH-RH
TOOLING ENGINEER NAME | FRANCISCO MELENDEZ
MOLD ARRIVAL DATE | 29/09/16
MOLD INCOMING INSP. DATE | 01/10/16
FREQUENCY FOR PM | 20,000 SHOTS
PRESS ASSIGNED | N/A
BACK TO INDEX